ELECTRICAL EQUIPMENT FOR

# HAZARDOUS ATMOSPHERES

CLASS I (GAS OR VAPOR)

GROUP:

A – 	ACETYLENE

B – 	HYDROGEN, MANUFACTURED GASES

C –       ETHYL – ETHER, ETHYLENE, CYCLE-PROPOANE

D –	GASOLINE, HEXANE, NAPHTHA

BENZINE, BUTANE, PROPANE, ALCOHOL,

LACQUER SOLVENT VAPORS, NATURAL GAS

DIVISION I								DIVISION II

HAZARD OF FIRE OR						HAZARD OF FIRE OR

EXPLOSION IS PRESENT					EXPLOSION IS PRESENT

NORMALLY								ONLY AS A RESULT OF AN

ACCIDENT

MOTORS MUST BE EXPLOSION				MOTORS:

PROOF WITH UNDERWRITER’S				SQ. CAGE MAY BE

LABEL								(a)  DRIPPROOF

- TEFC

**IMPORTANT NOTE: THIS DATA IS GREATLY CONDENSED.

IT SHOULD, HOWEVER CLAIRFY MANY QUESTIONS

REGARDING EXPLOSION-PROOF EQUIPMENT.

ELECTRICAL EQUIPMENT FOR

HAZARDOUS ATMOSPHERES

CLASS II (HAZARDOUS DUSTS)

GROUP:

E– 	METAL DUST (SPECIAL SEALS)

F – 	CARBON BLACK, COAL OR COKE DUST

G –      FLOUR, STARCH OR GRAIN DUST

DIVISION I								DIVISION II

HAZARD IS ALWAYS						(a) WHERE DUST DEPOSITS

PRESENT DUE TO NORMAL					ON ELEC. EQUIP. PREVENT

CONDITIONS							SAFE HEAT DISSIPATION

(DUST SUSPENDED IN THE 					(b) WHERE DEPOSIT OR

ATMOSTPHERE)							DUST MIGHT BE IGNITED

BY ARCS, OR BURNING MATERIAL

MOTORS MUST BE EXPLOSION				MOTORS:

PROOF WITH UNDERWRITER’S				SQ. CAGE MAY BE

LABEL								(a)  TEFC

(b) EXTERNALLY VENTILATED

**IMPORTANT NOTE: THIS DATA IS GREATLY CONDENSED.

IT SHOULD, HOWEVER CLAIRFY MANY QUESTIONS

REGARDING EXPLOSION-PROOF EQUIPMENT.

ELECTRICAL EQUIPMENT FOR

HAZARDOUS ATMOSPHERES

## CLASS III

FIBERS EASILY IGNITABLE BUT NOT

APT TO BE SUSPENDED IN AIR TO PRODUCE

IGNITABLE MIXTURES

EXAMPLES:

RAYON, NYLON, COTTON, SAW DUST, OR WOOD CHIPS

MOTORS:

SQ. CAGE MAY BE

- TEFC

- (b) EXTERNALLY VENTILATED

**IMPORTANT NOTE: THIS DATA IS GREATLY CONDENSED.

IT SHOULD, HOWEVER CLAIRFY MANY QUESTIONS

REGARDING EXPLOSION-PROOF EQUIPMENT.